Private Road with Public Easement Maintenance Standards

OCTOBER 2005

- Any private road receiving service would have a public easement signed by all property owners with fee interest in the road and have at least three year-round residential properties.

- Any private road with a public easement shall have a road association/spokesperson. On January 1 of each year or whenever the association has a change in elected/appointed positions, the association shall provide to the City Engineer’s Office a current contact list (phone number, e-mail address and mailing address) for at least the following:  President, Secretary and Road Commissioner.

- A private road with a Public Easement would receive winter plowing and sanding maintenance only, using City equipment and manpower or using a private contractor hired by the City.  In lieu of providing the services directly, the City reserves the right to establish a per mile cost for plowing and sanding and reimburse that amount to the Road Association. Said reimbursement amount would be reviewed every five (5) years and adjusted if necessary.

- Public easement roads would be plowed after City-owned public ways are passable. During spring thaw no plowing or sanding would be done due to the possibility of damaging the road. The City would not be responsible for any damage done to a public easement from plowing or traveling over the public easement.

- The road shall have a minimum width of 18 feet and 18” depth of well draining gravel.  For private roads receiving service prior to October 3, 2005, the City Engineer and Public Works Director may make exceptions to this standard on a case-by-case basis.  All new private roads with public easements accepted by the City for winter maintenance shall meet this requirement for minimum width and depth of gravel.

- The vertical and horizontal alignment of the private way shall be such that a commercial plow truck with sander can safely travel the entire length.

- The road shall have an adequate turnaround for commercial plow truck with sander.  A circlular turnaround or T-type turnaround is preferred.  Said turnaround shall be included in the public easement.

- The travel way shall be free of trees, branches, landscaping, rocks and other obstructions that could damage the vehicle performing the winter maintenance.  (Note: Major improvements such as tree removal on currently maintained private roads with public easements may be completed over a three-year period as agreed to by both the City and the Association.)

- In or around June of each year the City will inspect and provide the association with a report of the condition of the road. Items to be inspected include general road condition, erosion, road hazards, landscaping or other objects that have been placed in the agreed upon travel way.  The report shall contain a list of items that need to be addressed in order for the City to provide winter maintenance services for the coming season.  The Association shall be responsible for notifying the City Engineers office that said items have been remedied at which time a representative of the City shall inspect the work to make sure completed repairs are acceptable.  The City will not provide winter maintenance until any noted deficiencies are corrected.  The association may also be notified of other deficiencies if they are discovered at other times.

- All costs associated with the improvements necessary to meet these Private Road with Public Easement Maintenance standards shall be borne by the road association.

- All costs associated with the summer maintenance as well as general roadway improvements shall also be the responsibility of the road association.